## Slide 1: Handouts Phones Up

## Slide 2: Electricity
Potential difference (voltage): (energy source)provides the “push” that makes the charges move around the circuit
  Often a battery
  Commonly referred to as voltage
  This is analogous to gravitational potential energy.
    For batteries, the positive and negative charges are separated. A negative charge next to a negative is a high potential (they want to separate)also known as energy source
The unit for potential difference is VOLTS (V)

## Slide 3
SIMPLE CIRCUIT – diagram a circuit with a potential difference, switch, resistor, and an ammeter.

## Slide 4: Electricity
Circuits are usually drawn with a simplified diagram representing the power source or battery
The symbol used for potential difference (battery) in a circuit often looks like this:

## Slide 5: Electricity
A circuit is simply a closed loop through which charges can continuously move.

## Slide 6: Electricity
Closed circuit – the charges can flow from beginning to end
Open circuit – the charges cannot flow from beginning to end

## Slide 7: Electricity
Resistor: (load) resists the flow of energy and converts electrical energy into another form of energy
  E.g., light bulbs convert electrical energy into heat and light.

## Slide 8: Electricity
The symbol used for a resistor in a circuit often looks like this:
The unit for resistance / resistors is OHMS (Ω)

## Slide 9: Conductor vs Insulator
Conductor
Materials that permit electrons to flow freely from particle to particle
Transfers charge easily.
Insulator
Materials that impede the free flow of electrons from atom to atom and molecule to molecule.
Does NOT transfer charge.
REMEMBER! It is all about the electrons moving!!!
PROTONS (positive charges) DO NOT MOVE!!!

## Slide 10: Electricity
Wires –they connect the energy source and load. The charge flows through them.
Switch – opens and closes the circuit (turns it on and off)

## Slide 11: Electricity
A wire in a circuit is simply a straight line:
A switch in a circuit typically looks like this:

## Slide 12: Electricity
CURRENT: is the flow of charges. Current is measured in AMPERES, which we often shorten to AMPS (A).
Amps are measured by an ammeter. Often an ammeter is shown in a circuit diagram and looks like this:
A

## Slide 13: Starter Pg 92-93 YOU NEED A CALCULATOR
What is a short circuit?
Give three examples of a resistor.
What is the unit for current?
What two parts of the light bulb must be touched in order for the light bulb to light up?
What is the symbol for a resistor?
What is the difference between a closed and an open circuit?

## Slide 14: Common Symbols

## Slide 15: Series Circuit

## Slide 16: Series Circuit
In a series circuit, all points of resistance are connected on the same current path.
Old strands of Christmas lights were series circuits for safety reasons. If one bulb burned out, the whole string of lights went dead. This limited the risk of a spark from a shorted-out point causing a tree fire, but frustrated people when they had to check every bulb in the strand to find one that needed replacement.
The current is the same across every point in a series circuit.

## Slide 17
A single charge passes through each resistor consecutively.
As resistors are added the current decreases
As resistors are added overall resistance increases
If one resistor (bulb) goes out all of the bulbs will go out

## Slide 18: Equivalent Resistance
Equivalent resistance is the total amount of resistance in a circuit, which in series circuits is the sum of the resistance at every point across the circuit.
To calculate equivalent resistance in a series circuit, simply add the value of all the resistors together.

## Slide 19: Parallel Circuit
In a parallel circuit, each resistor has its own complete path from the positive terminal to the negative terminal.
This means that if one bulb burns out on the string of lights, all the other bulbs stay lit.
In a parallel circuit, voltage remains the same across each point.

## Slide 20: Parallel Circuit
Your house
Your phone
Your car

## Slide 21: Parallel Circuit
A single charge passes through only one resistor
As resistors are added, current increases
As resistors are added , overall resistance decreases
If one resistor (bulb) goes out the remaining ones get brighter

## Slide 22: Equivalent Resistance
To calculate equivalent resistance in a parallel circuit, add the inverse value of all the resistors together, and take the inverse of the sum.

## Slide 23: Example #1
Calculate the equivalent resistance in the series circuit shown below:
R = (R1) + (R2) + (R3) + …
R = (3) + (10) + (5)
R = 18Ω

## Slide 24: Example #2
Calculate the equivalent resistance in the parallel circuit shown below (round to the nearest tenth):
1/R = (1/R1) + (1/R2) + (1/R3) + …
1/R = (1/10) + (1/20) + (1/30) + (1/40)
1/R = (.21)
R = 4.8 Ω

## Slide 25: Example #3
A circuit is connected to a battery, and current flows through resistors of 4Ω, 6Ω, and 10Ω.
Draw the schematic representing this situation in a series circuit.
Draw the schematic representing this situation in a parallel circuit.
4 Ω
4 Ω
6 Ω
10Ω
6 Ω
10 Ω
10
Ω

## Slide 26: Examples #4-5
  If R1 = 3 Ω, R2 = 5 Ω, & R3 = 1 Ω, what is the equivalent resistance in the circuit?
    Req = 3 + 5 + 1 = 9 Ω
  If R1 = 4 Ω, R2 = 2 Ω, & R3 = 2 Ω, what is the equivalent resistance in the circuit?
    1/Req = ¼ + ½ + ½ = 1.25
    Req = 1/1.25 = 0.8 Ω

## Slide 27
https://www.youtube.com/watch?v=4thVCspAfK4
https://www.youtube.com/watch?v=a3Ftc_2iu7s&t=110s
https://www.youtube.co6m/watch?v=JeFyJN9qW48
https://www.youtube.com/watch?v=0j0wUOt9PK0

## Slide 28: CALCULATOR TODAY!! Handouts Phones Up Starter pg 92-93

## Slide 29: Starter pg 92-93 You need a calculator today
What is a series circuit? Define and give example.
What is a parallel circuit? Define and give example.

## Slide 30: STARTER pg 92-93
Of the below batteries which one would not work in a circuit? Why?
A. B.
Why does salt water work as a conductor while pure distilled water is an insulator?
What is the difference between a parallel and a series circuit?

## Slide 31: Electricity
Today we will:
Show how to calculate resistance, potential difference and power in a circuit using ohms law.
Demonstrate how to use ohms law to solve word problems.
Questions:
How does energy flow through a system?
How is electrical energy converted into other forms of energy?

## Slide 32: Electricity

## Slide 33: Electricity
OHM’s LAW – relates potential difference (V), current (I), and resistance (R):
Potential difference=volts
current=amps
Resistance=ohms

## Slide 34: Electricity
Applying Ohm’s Law:
If the resistor remains as is, what happens if I increase the potential difference (aka put a battery in the circuit with a higher voltage)?
the current increases
If the potential difference remains the same, but I decrease the value of the resistor, what happens?
the current increases

## Slide 35: Electricity
Low current vs High current

## Slide 36: Electricity
What is the current measured by the ammeter?
  I = V/R = 10/60 = 0.167 A

## Slide 37: Electricity
What is the potential difference in this circuit?
  V=IR=(2)(30)=60 V

## Slide 38: Electricity
What is the resistance in this circuit?
  R=V/I=6/2=3Ω
6

## Slide 39: Electrical Power Equation
P=VI
Power = Voltage X Current

## Slide 40: AC/DC
Direct Current: a constant stream of electrons in one direction.
DC example: a battery
https://www.youtube.com/watch?v=5UYF23C2Hew
Alternating Current: charges constantly reverse directions (60 times per second in the US)
AC example: 120 Volt wall outlet

## Slide 41: Starter on front of Ohm’s worksheet
What is the power of an electric circuit running with 1.2amps and 5 volts?
What is the potential difference when a circuit has 2 watts of power and 4 amps of resistance?
A student creates a circuit with a current of 15 amps and a voltage of 50v how much power will the circuit generate?
A circuit with 30v and 12 watts of power, what is the current?
If the current increases in a circuit what will happen to the power generated?

## Slide 42: TRANSFORMERS
You need a calculator today!
Put your phone away
Get out your homework and turn it in ASAP
Objective:
Identify the different types of transformers.
Review electrical energy and demonstrate understanding of electricity through a quiz.

## Slide 43
Transformers are composed of: iron core ring wrapped in coils
One coil is connected to an AC input voltage and is called the primary coil (input). The other coil is connected to an output circuit with a load resistance and is called the secondary coil(output).
The two coils are well insulated from each other and do not form a physical electrical connection.
Transformers can either step up or step down a voltage.
The constantly changing current induces a changing magnetic field in the core of the transformer.
If there are fewer coil turns in the secondary than the primary, it is a step-down transformer (high voltage to low).
Step-up is the opposite of step-down, it has fewer coil turns on input the than the output and changes the voltage from lower into higher.
https://www.youtube.com/watch?v=w9ugMmrCTg0

## Slide 44: Review
1. What type of current is used to power your house?
AC
2. If a circuit has a current of 4A and a power of 12W, what is the potential difference?
  V=P/I 12/4=3v
3. What is the resistance of a circuit with a voltage of 9v and a current of 7A?
R=V/I 9/7=1.29Ω
4. What is the equivalent resistance of a series circuit with resistors at 3Ω, 4 Ω, and 6 Ω?
R = (R1) + (R2) + (R3) 3+4+6=13Ω
5. 4.What is the equivalent resistance of a parallel circuit with resistors at 3Ω, 4 Ω, and 6 Ω?
  1/R = (1/R1) + (1/R2) + (1/R3) 1/R = (1/3) + (1/4) + (1/6) 1/.75=1.33Ω

## Slide 45: Electricity Circuit PROJECT